## Slide 1
An FPGA-based Accelerator for ShuffleNetV2
Yuhong Li, Ziyan Feng

## Slide 2
Outline
System Overview
Acclerator Architecture
Computation Engine
Result
Future Work

## Slide 3
System Overview
SD Card
ARM
CPU
DRAM
Accelerator
Data
Control
AXI HP
AXI Lite
Zync-7000 Soc
1.SD Card: Store the image and parameters and pass to DRAM
2.ARM CPU: Read parameters and images
Control the Accelerator
Calculate the execution time
3.Accelerator: On PL part, do calculation

## Slide 4
Outline
System Overview
Acclerator Architecture
Computation Engine
Result
Future Work

## Slide 5
Accelerator Architecture
Feature Map
Buffer 1
Weights
Buffer
DRAM
Computation
Engine
Accelerator
Feature Map 1
Feature Map 2
Ping-Pong Buffer
Feature Map
Buffer 2
Bias
Buffer
Conv(weights, bias, input, output)

## Slide 6
Outline
System Overview
Acclerator Architecture
Computation Engine
Result
Future Work

## Slide 7
Computation Engine: main structure
a
b
a: Basic Unit
b: Downsample Unit

## Slide 8
Computation Engine: Depthwise Conv
M
M
N
×
N
K
K
#pragma array_partition factor = a
#pragma loop unroll factor = a
N Loops -> N/a Loops
N/a

## Slide 9
Computation Engine: Pointwise Conv
Using Adder Tree
Calculate one element:
N Loop -> log2(N)
M
M
N
×
1
1
N×P
P

## Slide 10
Outline
System Overview
Acclerator Architecture
Computation Engine
Result
Future Work

## Slide 11
Experiment Result
Testing Accuracy Curve

## Slide 12
Experiment Result
weight type | bias type | feature map type | activation type | accuracy | if retrain
floating32 | floating32 | floating32 | ReLU4 | 90.37 | -
fix<1,6> | fix<1,6> | fix<1,6> | ReLU4 | 87.308 | -
fix<1,6> | fix<1,6> | fix<1,6> | ReLU4 | 88.51 | yes

## Slide 13
Experiment Result
Resourse | Used | Avaible | Ratio (%)
DSP | 196 | 220 | 89%
BRAM | 268 | 280 | 95%
FF | 80864 | 106400 | 76%
LUT | 37247 | 53200 | 70%
Verion | Time(Cycle)
CPU | 33,860 k
HLS without optimization | 110,591 k
HLS with fixed point | 83,125 k
Final time | 15,143k
Final speedup | 2.236x

## Slide 14
Outline
System Overview
Acclerator Architecture
Computation Engine
Result
Future Work

## Slide 15
Future Work
Double Buffer for weights
More Complex Algorithm for Matrix Multiplication
(Adder Tree and Matrix Division)
16-bit Quantization (Selected by previous work)

## Slide 16
Thank you